## Slide 1: Arduino Programming

## Slide 2: Agenda
What is Arduino?
What can I make with Arduino?
Getting started
Digital Inputs and Outputs
Analog Inputs and Outputs
Motors
Putting It All Together
Summary

## Slide 3: What is Arduino?
“Arduino is an open-source electronics prototyping platform based on flexible, easy-to-use hardware and software. It's intended for artists, designers, hobbyists, and anyone interested in creating interactive objects or environments.“
  http://www.arduino.cc/

## Slide 4: What is Arduino?
A programming environment for Windows, Mac or Linux
A hardware specification
Software libraries that can be reused in your programs
All for FREE!*
* Except the price of the hardware you purchase

## Slide 5: Arduino UNO
The most commonly used Arduino board
We will be using this board in this workshop

## Slide 6: Arduino UNO
Microprocessor – Atmega328
  16 Mhz speed
  14 Digital I/O Pins
  6 Analog Input Pins
  32K Program Memory
  2K RAM
  1k EEPROM
Contains a special program called a “Bootloader”
  Allows programming from USB port
  Requires 0.5K of Program Memory

## Slide 7: Arduino Shields
Many companies have created Shields that can be used with Arduino boards
Examples
  Motor/Servo interface
  SD memory card interface
  Ethernet network interface
  GPS
  LED shields
  Prototyping shields

## Slide 8: What can I make with Arduino?
Alarm Clock
http://hackaday.com/2011/07/04/alarm-clock-forces-you-to-play-tetris-to-prove-you-are-awake/

## Slide 9: What can I make with Arduino?
Automatic Pet Water Dispenser
http://hackaday.com/2011/05/24/automated-faucet-keeps-your-cat-watered/

## Slide 10: Let’s GO!
Get the hardware
  Buy an Arduino UNO
  Buy (or repurpose) a USB cable
Get the software
  http://arduino.cc/en/GuideHomePage
Follow the instructions on this page to install the software
Connect the Arduino to your computer
You are ready to go!

## Slide 11: The IDE
This is your ‘Arduino’ software.
Download it for free: https://www.arduino.cc/en/Main/Software
It makes programming easier than command line tools of Ye Olden Days.

## Slide 13: IDE Tips and ‘Gotchas’
If you can’t upload, check Tools->Port
There’s a wealth of example code: File -> Examples
Use the Serial Monitor for debugging, but keep in mind this can affect your program (especially where timing is concerned!)

## Slide 14: Lab 1
Blink the onboard LED by uploading File->Examples->Basic->Blink
Congratulations!!!

## Slide 15: Review the Sketch
/*
Blink
. . .
*/
// set the LED on
// wait for a second
These are comments
The computer ignores them
Humans can read them to learn about the program

## Slide 17: Review the Sketch
void setup() {
pinMode(13, OUTPUT);
}
Brackets { and } contain a block of code
  Each line of code in this block runs sequentially
void setup() tells the program to only run them once
  When the board turns on
  When the reset button is pressed

## Slide 18: Review the Sketch
void setup() {
pinMode(13, OUTPUT);
}
Tells the Arduino to setup pin 13 as an Output pin
Each pin you use needs be setup with pinMode
A pin can be set to OUTPUT or INPUT

## Slide 19: Review the Sketch
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
void loop () runs the code block over and over until you turn off the Arduino
This code block only runs after setup is finished

## Slide 20: Review the Sketch
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
HIGH tells the Arduino to turn on the output
LOW tells the Arduino to turn off the output
13 is the pin number

## Slide 21: Review the Sketch
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delay(1000);
}
Code runs very fast
Delay tells the Arduino to wait a bit
1000 stands for 1,000 milliseconds or one second

## Slide 22: Change the Sketch
void loop() {
digitalWrite(13, HIGH);
delay(500);
digitalWrite(13, LOW);
delay(500);
}
Change the 1000’s to 500
Upload the code to the Arduino
What happens now?

## Slide 23: Arduino Digital Pins
These pins are used to communicate with the outside world
When an output pin is HIGH, it can provide 5V at 40mA maximum
  Trying to get more than 40mA out of the pin will destroy the Microprocessor!
When the output pin is LOW, it provides no current
You can use a transistor and/or a relay to provide a higher voltage or more current

## Slide 24: Connecting a new LED
Most LEDs will work with 5V at 20mA or 30mA
Make sure to check them before connecting to your Arduino! – Use your volt meter
An LED requires a resistor to limit the current
  Without the resistor, the LED will draw too much current and burn itself out

## Slide 25: Connecting a new LED
LEDs are polarized devices
One side needs to be connected to + and one side needs to be connected to –
If you connect it backwards, it will not light
Usually:
  Minus is short lead and flat side
  Plus is long lead and rounded side
A resistor is non-polarized
  It can be connected either way

## Slide 26: Lab 2
Connect the two LEDs on the breadboard
Modify the code to blink the second LED, too
Blink them all

## Slide 27: Input
The pins can be used to accept an input also
Digital pins can read a voltage (1) or no voltage (0)
Analog pins can read voltage between 0V and 5V. You will read a value of 0 and 1023.
Both of these return a value you can put into a variable and/or make decisions based on the value

## Slide 28: Input
Example
int x;
x = digitalRead(2);
if ( x == HIGH ) {
digitalWrite(13, HIGH);
} else {
digitalWrite(13, LOW);
}

## Slide 29: Push Button
A push button can be connected to a digital pin
There is an open circuit normally
There is a closed circuit when pressed
If connected between 5V and a pin, we get 5V when pressed, but an open circuit when not pressed
This is a problem – we need 0V when not pressed

## Slide 30: Push Button
There is a solution
A resistor to 5V will make the pin HIGH when the button is not pressed
Pressing it will make the pin LOW
The resistor makes sure we don’t connect 5V directly to Ground

## Slide 31: Push Button
This is a common method for using push buttons
The resistor is called a “Pull Up Resistor”
The Arduino has built in pull up resistors on the digital pins
We need to enable them when we need them

## Slide 32: Push Button
This code enables the pull up resistor:
    pinMode(2, INPUT_PULLUP);

## Slide 33: Lab 3
Connect a push button
Load the basic button code (File->Examples->Digital->Button
Turn LEDs on/off based on button press
Load the ‘Debounce’ Example (File->Examples->Digital->Debounce). Experiment with changing the value of the ‘debounceDelay’ variable.

## Slide 34: Other Sensors/Devices
There are many other devices you can connect to an Arduino
  Servos to move things
  GPS to determine location/time
  Real Time Clock to know what time it is
  Accelerometers
  LCD displays
  Memory cards to store sounds, images, readings
  Distance Sensors
  More!

## Slide 35: Let’s Go Analog
So far we’ve dealt with the on/off digital world.
Many interesting things we want to measure (temperature, light, pressure, etc) have a range of values.

## Slide 36: The Potentiometer
Very simple analog input – used to control volume, speed, and so on.
It allows us to vary two resistance values.

## Slide 37: The Serial Port
You can communicate between the Arduino and the computer via the USB cable.
This can help you out big time when you are debugging.
It can also help you control programs on the computer or post information to a web site.
    Serial.begin(9600);
    Serial.println(“Hello World.”);

## Slide 38: Lab 3
Connect potentiometer (see next page)
Upload and run code (File->Examples->Analog->AnalogInOutSerial
Turn the knob
Watch the value change in the Serial Monitor
Add an LED on Pin 9. Watch the brightness change as you turn the knob.

## Slide 40: The Voltage Divider
There are many, many sensors based on varying resistance: force sensors, light dependent resistors, flex sensors, and more.
To use these you need to create a ‘voltage divider’.
These are based on Ohm’s Law: V = IR

## Slide 41: The Voltage Divider

## Slide 42: Light Sensor
R2 will be our photocell
R1 will be a resistor of our choice
Rule of thumb is: R1 should be in the middle of the range (but don’t get hung up on an exact value. Experiment!)

## Slide 43: Lab 4
Wire up the photocell (next page)
Same code as Lab 3
Take note of the max and min values
Try to pick a value for a dark/light threshold.

## Slide 45: Analog Output
Flashing a light is neat, but what about fading one in and out?
Or changing the color of an RGB LED?
Or changing the speed of a motor?

## Slide 46: PWM (Pulse Width Modulation)

## Slide 47: Lab 5
Wire up the Breadboard
Load the code (File->Examples->Analog->Fading). Take note of the for loop.
Watch the light fade in and out
Experiment with the code to get different effects

## Slide 48: Making Things Move
So far we’ve communicated with the world by blinking or writing to Serial.
Let’s make things move!

## Slide 49: Lab 6: Neopixels
Neopixels are Adafruit’s rebranding of WS2812B Addressable RGB LEDs (‘Neopixel’ is way catchier)
You can chain them together and control as many pixels as you want (or can power) with a single pin!
You can buy strips and rings of them.
However, the code is not built in to the Arduino IDE, so you have to install a library
This is something you often need for new parts

## Slide 50: Wire it Up
Wire it up as shown below. (Wire color is important - your Neopixels look different).

## Slide 51: Installing the Library
Get the library from https://github.com/adafruit/Adafruit_NeoPixel
Go to Sketch->Import Library->Add Library
Find the file you just downloaded
Restart the IDE after Importing it (otherwise you won’t see the examples)

## Slide 52: Code
Open the ‘NeopixelsWorkshop.ino’ file in the ‘NeopixelsWorkshop’ folder.
  #include <Adafruit_NeoPixel.h>
  // Which pin on the Arduino is connected to the NeoPixels?
  #define PIN 7
  // How many NeoPixels are attached to the Arduino?
  #define NUMPIXELS 2
  // When we setup the NeoPixel library
  // we tell it how many pixels, and which pin to use
  // to send signals.
  Adafruit_NeoPixel pixels = Adafruit_NeoPixel(NUMPIXELS, PIN, NEO_GRB + NEO_KHZ800);

## Slide 53: …and more code
Our ‘strip’ is an object. We call functions or ‘methods’ tied to it:
  void setup() {
    strip.begin();
    strip.show(); // Initialize all pixels to 'off'
  }

## Slide 54: …and more
To set a pixel’s color, specify the number (start at zero). Do this for as many pixels as you want, then call the function to show these colors.
  pixels.setPixelColor(1, pixels.Color(i,255-i,0));
  pixels.show();
Can you guess what this program does before you upload it?
Have fun…be creative!

## Slide 55: Other Senses
With a piezo or small speaker, your Arduino can make some noise, or music (or ‘music’).
As with game controllers, vibrating motors can stimulate the sense of touch (this is called a ‘haptic interface’).
Arduino projects exist that involve smell (breathalyzer, scent generators).
For taste…KegBot? ZipWhip’s cappuccino robot?

## Slide 56: Lab 7 – The Light Theremin
Combine previous projects (photocell and the piezo playing music) to create an instrument that generates a pitch based on how much light is hitting the photocell
Feel free to get really creative with this.
For extra creativity points, do something totally different.

## Slide 57: Summary
We have learned
  The Arduino platform components
  how to connect an Arduino board to the computer
  How to connect LEDs, buttons, a light sensor, a piezo buzzer, and servos
  How to send information back to the computer

## Slide 58: Resources
http://www.arduino.cc
Getting Started With Arduino (Make: Projects) book
Arduino: A Quick Start Guide book
The adafruit learning system: https://learn.adafruit.com/

## Slide 59: Where to buy stuff
Adafruit http://www.adafruit.com/
Spark Fun http://www.sparkfun.com/
Maker Shed http://www.makershed.com/
Digikey http://www.digikey.com/
Mouser http://www.mouser.com/
Radio Shack http://www.radioshack.com/
Find parts: http://www.octopart.com/
Sometimes Amazon has parts too
Ebay can have deals but usually the parts are shipped from overseas and take a long time

## Slide 60: Where to get help
http://arduino.cc/forum/
Your local Hackerspace!

## Slide 61: Electronics 101
Electronic devices depend on the movement of electrons
The amount of electrons moving from one molecule to another is called Current which is measured in Amps
Batteries provide a lot of electrons that are ready to move
The difference in potential (the number of free electrons) between two points is called Electromotive Force which is measured in Volts

## Slide 62: Electronics 101
Materials that allow easy movement of electrons are called Conductors
  Copper, silver, gold, aluminum are examples
Materials that do not allow easy movement of electrons are called Insulators
  Glass, paper, rubber are examples
Some materials are poor conductors and poor insulators.
  Carbon is an example

## Slide 63: Electronics 101
Materials that aren’t good conductors or good inductors provide Resistance to the movement of electrons
Resistance is measured in Ohms

## Slide 64: Electronics 101
Electrons flow from the negative terminal of the battery through the circuit to the positive terminal.
But – when they discovered this, they thought current came from the positive terminal to the negative
This is called conventional current flow
I
Oops!

## Slide 65: Electronics 101
There needs to be a complete circuit for current to flow
No Flow!
Current will Flow!

## Slide 66: Electronics 101
Volts, Amps and Ohms are related
This is called Ohms Law
I = Current in Amps
E = EMF in Volts
R = Resistance in Ohms

## Slide 67: Electronics 101
Example
BAT = 9 volts
R1 = 100 ohms
How many amps?
I = 0.09 Amps or 90mA

## Slide 68: Electronics 101
When dealing with really big numbers or really small numbers, there are prefixes you can use
  k = kilo = 1,000 (e.g. 10 kHz = 10,000 Hz)
  M = mega = 1,000,000 (e.g 1 MHz = 1,000 kHz)
  m = milli = 1/1,000 (e.g 33mA = 0.033A)
  u = micro = 1/1,000,000 (e.g 2uV = 0.000002V)
  n = nano = 1/1,000,000,000
  p = pico = 1/1,000,000,000,000